SAFETY DATA SHEET

Section 1.		Identification of the material and the supplier

Product: 	GreenManTM

Item Code:

Product Use: 	Non-selective herbicide

Restriction of Use:	Refer to Section 15

New Zealand Supplier:	Element Raw Materials Ltd

Address:		573 Halkett Road

RD1, Christchurch, 7671

Telephone:	+64 3 3181 262

Emergency Telephone:	0800 764 766 (National Poison Centre)

Date of SDS Preparation:	19 October 2016

Section 2.		Hazards Identification

This substance is hazardous according to the HSNO (Minimum Degrees of Hazard) Regulations 2001

EPA Approval No:  HSR000827

###### Pictograms

Irritant             Corrosive

Signal Word:  DANGER

| HSNO Classification | Hazard Code | Hazard Statement | GHS Category |
| --- | --- | --- | --- |
| 6.3A | H315 | Causes skin irritation. | Category 2 |
| 8.3A | H318 | Causes serious eye damage. | Category 1 |
| 9.1C | H412 | Harmful to aquatic life with long lasting effects. | Category 3 |

| Prevention Code | Prevention Statement |
| --- | --- |
| P102 | Keep out of reach of children. |
| P103 | Read label before use. |
| P264 | Wash hands thoroughly after handling. |
| P273 | Avoid release to the environment. |
| P280 | Wear protective clothing. |

| Response Code | Response Statement |
| --- | --- |
| P101 | If medical advice is needed, have product container or label at hand. |
| P310 | Immediately call a POISON CENTER or doctor/physician. |
| P362 | Take off contaminated clothing and wash before re-use. |
| P302 + P352 | IF ON SKIN: Wash with plenty of soap and water. |
| P305 + P351+P338 | IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. |
| P332 + P313 | If skin irritation occurs: Get medical advice/ attention. |

| Storage Code | Storage Statement |
| --- | --- |
| None allocated |  |

| Disposal Code | Disposal Statement |
| --- | --- |
| P501 | Dispose of according to Local Regulations or Authorities |

#### Section 3.		Composition / Information on Ingredients

| Ingredients | Wt% | CAS NUMBER. |
| --- | --- | --- |
| Fatty Acids (from Rape Seed) | 65 | Proprietary |
| Other non-hazardous ingredients | 35 | Proprietary |

Section 4.		First Aid Measures

Routes of Exposure:

If in Eyes	Rinse cautiously with water for 15 minutes. Remove contact lenses, if

present and easy to do. Continue rinsing.  If eye irritation persists: Get medical advice.

If on Skin	Wash with plenty of soap and water. Take off contaminated clothing and wash before re-use.  If skin irritation occurs: get medical advice/attention.

If Swallowed	Rinse mouth. Never give anything to the mouth of an unconscious person.   Wash the mouth with clean water and give them several glasses of water to drink to disperse the ingested material. Induce vomiting. Get medical attention at once.

If Inhaled	Remove person to fresh air. Remove contaminated clothing and loosen             remaining clothing. Allow person to assume most comfortable position                                                    and keep warm. Keep at rest until fully recovered. Get medical advice if             breathing becomes difficult.

Section 5.		Fire Fighting Measures

| Hazard Type | Non Flammable |
| --- | --- |
| Hazards from combustion products | None known. |
| Suitable Extinguishing media | Carbon Dioxide, Sand, Dry Chemical, and Foam. |
| Precautions for firefighters and special protective clothing | Fire fighters should be equipped with self-contained breathing apparatus to protect against potentially toxic and irritating fumes. |
| HAZCHEM CODE | None Allocated |

Section 6.		Accidental Release Measures

Wear protective equipment as detailed in Section 8.  Clear area of any unprotected personnel.

Spills should be swept up and placed in appropriate containers for disposal. Spill area can become slippery.  Wash spill area with soap and water.  Do not wash into sewers or into any body of water. Advise water authority if spillage has entered watercourses or drainage system.

Section 7.		Handling and Storage

Precautions for Handling:

- Read label before use.

- Wash hands thoroughly after handling.

- Avoid release to the environment.

- Do not contaminate water, food, or feed by storing or disposal.

- Wear protective clothing.

Precautions for Storage:

- Store away from incompatible materials listed in Section 10.

- Keep away from children.

- Store in a dark, cool and arid place to keep away from high temperature and strong sunshine.

Section 8		Exposure Controls / Personal Protection

WORKPLACE EXPOSURE STANDARDS (provided for guidance only)

TWA	STEL

Substance		ppm   mg/m3	ppm   mg/m3

No ingredients have exposure limits.

Workplace Exposure Standard – Time Weighted Average (WES-TWA).The time-weighted average exposure standard designed to protect the worker from the effects of long-term exposure.  Workplace Exposure Standard – Short-Term Exposure Limit (WESSTEL). The 15-minute average exposure standard. Applies to any 15- Minute period in the working day and is designed to protect the worker against adverse effects of irritation, chronic or irreversible tissue  change, or narcosis that may increase the likelihood of accidents. The WES-STEL is not an alternative to the WES-TWA; both the short-term and time-weighted average exposures apply.

Engineering Controls

Not normally required when used as directed on the product label.

Personal Protection

| Eyes | Wear goggles or safety glasses with side shields. Avoid wearing contact lenses. |
| --- | --- |
| Hands and Skin | Wear appropriate PPE: PVC gloves and polycotton coveralls and waterproof shoes. |
| Respiratory | Respiratory protection should not be required for normal use and handling. During abnormal exposures or when there is a chance that Acceptable Exposure Limit will be exceeded, use an approved dust respirator. |
| General | After use and before eating, drinking or smoking, wash hands, arms and face thoroughly with soap and water. |

Section 9		Physical and Chemical Properties

| Appearance | Light yellow liquid |
| --- | --- |
| Odour | Characteristic |
| Odour Threshold | Not available |
| pH | 3.5 – 5.0 |
| Boiling Point | 2530C |
| Melting Point | Not available |
| Freezing Point | Not available |
| Flash Point | Not available |
| Flammability | Not flammable or combustible |
| Upper and Lower Explosive Limits | Not available |
| Vapour Pressure | Not available |
| Vapour Density | Not available |
| Density | 0.92 – 0.96kg/l |
| Solubilities | Forms an emulsion in water |
| Partition Coefficient: | Not available |
| Auto-ignition Temperature | Not available |
| Decomposition Temperature | Not available |
| Kinematic Viscosity | Not available |
| Refractive index | 1.431 – 1.433 |

Section 10.	Stability and Reactivity

| Stability of Substance | This product is stable under normal conditions. |
| --- | --- |
| Conditions to Avoid | Avoid extremes of temperature. |
| Incompatible Materials | None under normal use conditions. Under abnormal conditions, avoid alkali. |
| Hazardous Decomposition Products | None under normal conditions of storage and use. |

Section 11		Toxicological Information

Acute Effects:

| Swallowed | Not applicable. LD 50 = >5000mg/kg |
| --- | --- |
| Dermal | Not applicable. LD50 = >5000mg/kg |
| Inhalation | Not applicable. |
| Eye | Causes serious eye damage. |
| Skin | Causes skin irritation. |

Chronic Effects:

| Carcinogenicity | Not applicable. |
| --- | --- |
| Reproductive Toxicity | Not applicable. |
| Germ Cell Mutagenicity | Not applicable. |
| Aspiration | Not applicable. |
| STOT/SE | Not applicable. |
| STOT/RE | Not applicable. |

Section 12.	Ecotoxicological Information

HSNO Classes:	9.1C = Harmful to aquatic life with long lasting effects.

| Persistence and degradability | No data available |
| --- | --- |
| Bioaccumulation | No data available |
| Mobility in Soil | The half-life of vegetable fats in soil is about 2-3 days, and there is no residue after seven days. |
| Other adverse effects | No data available |

Section 13.	Disposal Considerations

Disposal Method:	Triple rinse container and dispose according to Local regulations. Unwanted product should be disposed of as a hazardous waste according to local and national regulations.

Disposal methods to avoid: Do not allow to enter waterways.

Section 14		Transport Information

This product is NOT classified as a Dangerous Good for transport in NZ ; NZS 5433:2012

Section 15		Regulatory Information

EPA Approval Code:  HSR000827

HSNO Classification:  6.3A, 8.3A, 9.1C

Trigger quantities for this substance:

| HSNO Controls | Trigger Quantity |
| --- | --- |
| Approved Handler | Not required |
| Location Certificate | Not required |
| Tracking Trigger Quantities | Not required |
| Signage Trigger Quantities | 1000L (9.1C) |
| Emergency Response Plan | 1000L (9.1C) |
| Secondary Containment | 1000L (9.1C) |
| Restriction of Use | This substance must not be applied onto or into water. |

Section 16		Other Information

Glossary

EC50	Median effective concentration.

EEL	Environmental Exposure Limit.

EPA	Environmental Protection Authority

HSNO	Hazardous Substances and New Organisms.

LC50	Lethal concentration that will kill 50% of the test organisms 	inhaling or ingesting it.

LD50	Lethal dose to kill 50% of test animals/organisms.

LEL	Lower explosive level.

OSHA	American Occupational Safety and Health Administration.

TEL	Tolerable Exposure Limit.

TLV	Threshold Limit Value-an exposure limit set by responsible 	authority.

UEL	Upper Explosive Level

WES	Workplace Exposure Limit

1. HSNO Approved Code of Practice: Preparation of Safety Data Sheets, September 2006.

Disclaimer

This document has been issued by TCC (NZ) Ltd and serves as their Safety Data Sheet ('SDS'). It is based on information concerning the product which has been provided to TCC (NZ) Ltd or obtained from third party sources and is believed to represent the current state of knowledge as to the appropriate safety and handling precautions for the product at the time of issue. Further clarification regarding any aspect of the product should be obtained directly from the manufacturer. While TCC (NZ) have taken all due care to include accurate and up-to-date information in this SDS, it does not provide any warranty as to accuracy or completeness. As far as lawfully possible, TCC (NZ) Ltd accept no liability for any loss, injury or damage (including consequential loss) which may be suffered or incurred by any person as a consequence of their reliance on the information contained in this SDS

The information herein is given in good faith, but no warranty, express or implied is made.

Please contact the New Zealand distributor, if further information is required.

Issue Date:		19 October 2016            Review Date:		19 october 2021